## Slide 1: Fall Protection Exception
WWW.SFICOMPLIANCE.COM
CUSTOMERSERVICE@SFICOMPLIANCE.COM
800-727-5051

## Slide 2: Subpart M, Fall Protection: 1926.500(a)(1)
This subpart sets forth requirements and criteria for fall protection in construction workplaces covered under 29 CFR part 1926. Exception: The provisions of this subpart do not apply when employees are making an inspection, investigation, or assessment of workplace conditions prior to the actual start of construction work or after all construction work has been completed.
Any employee?
Any inspection?
Any time?

## Slide 3: Implementation
Often times taken at face-value, or
Misinterpreted, or
Misapplied, or
All of the above.
Commenter to final fall protection rule stated:
  “Superintendents, foremen, and other company officials will never have to be protected during the entire job, because they will say that they are only inspecting.”

## Slide 4: Letter of Interpretation
“Interpretation of OSHA Fall Protection Exemption (29 CFR § 1926.500(a)(1)) during inspection, investigation, and assessment activities.”
Provides detail regarding the intent of the provision.
  This is what it says, but this is what it means.

## Slide 5: Intent: Who, When, Why
Pre-construction – before any work has begun.
  Estimators
  Engineers
Post-construction – after all work is complete.
  Quality
  Warranty
  Owners
Justification:
  Inspectors “are not continually or routinely exposed to fall hazards tend to be very focused on their footing, ever alert and aware of the hazards associated with falling.”
  Inspections “are normally conducted in good weather”
  “Such requirements would impose an unreasonable burden on employers without demonstrable benefits.”

## Slide 6: Intent: Who, When, Why
Does NOT apply to before work has begun/after work is complete for the day.
  Ex: Workers accessing roof daily should be able to tie off before exposure. Workers should remain tied off until clear of the exposure.
Who does this NOT apply to?
  Anyone (trades) performing actual construction work.
  Inspections necessitating extended exposure to “danger zone”
  Inspections with excessive use of tools (distraction)
  Inspections taking place during active construction

## Slide 7: Intent: Who, When, Why
Consideration should be given to:
  Duration – should be short
    No definition given
    Justification is a worker installing fall protection would be exposed to falls longer than an inspector would.
  Proximity to hazard or “danger zone”
    Inspecting nail pattern at center of deck vs. inspecting coping on short parapet
From Final Rule: Safety Standards for Fall Protection in the Construction Industry (08/09/1994)
  “If inspections are made while construction operations are under way, all employees who are exposed to fall hazards while performing these inspections must be protected as required by subpart M.”

## Slide 8: Steve Mullen, CSP, ARM, CRIS steve@sficompliance.com 602-316-9038 sficompliance.com
Notes: $865 million in restoration and rebuild costs (direct costs)
At one point, estimated $2 million lost daily in tourist revenue (indirect costs)
Construction at cathedral suspected to be a cause since the fire started
In every picture there is a TREMENDOUS AMOUNT OF SCAFFOLDING
Recently new theory has come forward blaming electric bells installed 15 years ago – frayed wires
Who is publicizing this theory – scaffold owner